## Slide 1: CPU
Key Revision Points

## Slide 2: Components
Control Unit
  Executes program instructions
  Controls other components in the CPU (e.g. the ALU) and outside the CPU (e.g. RAM)
Arithmetic Logic Unit
  Does all the calculations
Registers
  Temporary storage in the CPU for instructions and data
  Very fast but hold tiny amounts of data

## Slide 3: Registers
Program Counter – memory address of next instruction to fetch. Updated after each cycle
Memory Address Register - memory address of next instruction to fetch. Copied from the program counter
Memory Data Register – data or instruction fetched from the address above
Accumulator – in the ALU. Holds results of intermediate calculations

## Slide 4: Fetch Decode Execute
Control unit fetches the next instruction or data from the memory location the program counter (and the MAR) points to
The instruction or data is stored in the MDR
As the data or instruction is in binary it needs to be translated or decoded
The ALU then carries out or executes the instruction
The result is sent back to the control unit, the program counter is incremented and the process repeats until there are no more instructions

## Slide 5: Performance - Clock
Clock/Clock Speed
  CPU contains quartz clock
  CPU can execute one instruction per pulse of the clock
  Measured in GHZ: 1 GHz processor = 1 billion instructions per second
  May not be able to achieve this if RAM can’t send instructions fast enough so need cache…

## Slide 6: Performance - Cache
Cache
  Fast memory on or near the CPU.
  Faster than RAM so reduces bottlenecks
  Stores frequently used data so the CPU can access it quickly

## Slide 7: Performance - Cores
Core
  Separate processor in the CPU e.g. quad core = a CPU with 4 processors
  2GHz quad core = 8 billion instructions per second i.e. 2bn per core x 4 cores
  Allows parallel processing – more than one operation at the same time
  May not be able to achieve this if not all instructions can be carried out simultaneously

## Slide 8: Textbook and Firefly
Textbook pages 2, 3, 5, 12
Firefly (including knowledge organiser)
http://wilmslowhigh.fireflycloud.net/computing/year-11/computer-systems/the-cpu1
http://wilmslowhigh.fireflycloud.net/computing/year-11/computer-systems/the-cpu2