## Slide 1: Memory
Key Revision Points

## Slide 2: Random Access Memory (RAM)
Main memory where data, files programs are stored while in use
  When you run a program it is copied from the hard disk into RAM
  When the computer boots the OS (e.g. Windows is copied into RAM)
Volatile – requires power to retain its data. Storage is temporary.
Slower than cache but faster than secondary storage
RAM comes on “sticks” or modules that plug into slots on the motherboard
  Easy to replace/upgrade

## Slide 3: More/Less RAM?
If computer doesn’t have enough RAM it will run slowly – has to swap data in and out of slower virtual memory
More RAM allows you to run more applications simultaneously – can all be loaded into main memory
Generally the more RAM the better but…
If a PC already has plenty of RAM (to run everything the user wants) adding more may not improve performance

## Slide 4: Read Only Memory
Non volatile – does not require power to retain data. Storage is permanent
ROM chips are built-in to the motherboard
BIOS (Basic Input Output System) is held in ROM
  Instructions computer needs to boot up properly
  Self checks CPU/RAM  Loads drivers for basic input/output hardware  Loads OS into RAM
Needs to be in ROM or instructions lost when the computer turned off. Wouldn’t know how to boot next time it was turned on!
Although ROM is read only it can be updated by “flashing”

## Slide 5: Other Uses of ROM
Firmware = hardware specific software built into a device (the BIOS is firmware)
Many devices that use embedded systems e.g. microwave store their software/firmware on ROM chips

## Slide 6: Virtual Memory
Part of the secondary storage (e.g. the hard drive) used like additional RAM
Needed when RAM is full because…
  Too many applications open
  Memory intensive operations being performed
Data transferred temporarily into virtual memory to free up RAM
May make the computer slow to respond – due to constantly moving data between VM and RAM

## Slide 7: Speed?
Complete the table with the different types of memory in a computer system
Virtual memory, Registers, RAM, ROM, Cache
Fastest |  |  |  | Slowest

## Slide 8: Textbook and Firefly
Textbook pages 4,12
Firefly
http://wilmslowhigh.fireflycloud.net/computing/year-11/computer-systems/memory